## Slide 1
U.S. Army ATR Training Program
10 US Code 2302 (PL 102-484, S326)
Army Acquisition Executive Environmental Support Office

## Slide 2
ELIMINATE ALL DEPENDENCY
ON ODS – CLASS I AND II
READINESS ISSUE
Army Dependency
on ODS …
In Weapon Systems and Equipment Is a
The Goal of the Army ODS Program Is to

## Slide 3
What is the Ozone Layer?
  Response to Concerns
    Army Applications
Part 1

## Slide 4
What Is the
Ozone Layer?
Stratospheric Ozone
Discovery of Ozone Depletion
Ozone Depleting Substances
Typical ODS
DoD Share of Ozone Depletion

## Slide 5
Stratospheric Ozone
Oxygen radical (O3 )
Ground Level = Smog
30x Concentration @ 12-19 Miles
  Reflects Harmful UV-B Radiation
  “Cools” the Atmosphere
O
O
O
Ozone Layer

## Slide 6
Ozone Layer
200 DU (1980)
75 DU (1995)
115 DU (2014)
10,000 ppb
98% UV-B

## Slide 7
Discovery of Ozone Depletion
1970s -- CFCs Used as Tracers -- Study of Cl Rx w/Ozone
1980s -- CFCs Longevity in Air -- Ozone Column
1990s -- Direct Measurement -- -- “Ozone Holes” -- Computer Models -- Start of Public Outcry
Ozone Layer

## Slide 8
Fire Suppression
Refrigeration/Air-Conditioning
Cleaning/Degreasing
OZONE
DEPLETING SUBSTANCES
HBrFCs
BrFCs
HCFCs
CFCs
Ozone Layer

## Slide 9
Typical ODS
Fire Suppressants: Halon 1211, Halon 1301
Refrigerants (Class I): R-11, R-12, R-500, R-502
Refrigerants (Class II): R-22, R-123
Solvents (Class I): Methyl Chloroform, CFC-113
Solvents (Class II): HCFC-141b, HCFC-225
Ozone Layer

## Slide 10: DoD ODS Use in 1986 vs Total U.S. Production
SOURCE: Alliance for Safe CFC Policy
Ozone Layer

## Slide 11: Response to Concerns
Montreal Protocol
Clean Air Act Amendments of 1990
DoD Directive 6050.9
U.S. Army
General Officers Steering Committee
HQ DA LTR 200-90/92-1 (expired)
Strategic Guidance & Planning
AR 200-1 & AP 200-1
Policy Memoranda
Defense Authorization Act for FY93

## Slide 12: Response to Concerns
Montreal Protocol
International Treaty to Protect Ozone Layer
Signed by 24 Nations - September 1987
Ratified by US Senate - April 1988
      London Amendment
      Copenhagen Amendments
      Vienna Amendments

## Slide 13: London Amendments September 1990
Signed by 68 Nations
Added Phase-out Schedule
  Halons / CFCs - 2000
  Carbon Tetrachloride - 2000
  Methyl Chloroform - 2005
  HCFCs (Class II) - 2020
Response to Concerns

## Slide 14: Copenhagen Amendments November 1992
Accelerated Production Phase-outs
  Halons 01 Jan 94
  CFCs 01 Jan 96
Expanded Controlled Substances
  34 HCFCs (phase-out by 2030)
  34 HBFCs (phase-out by 1996)
  Methyl Bromide
Response to Concerns

## Slide 15: Vienna Amendments December 1995
Requirements for Developing Nations
Accelerated Phase-out for Developed
  Methyl Bromide 2010
  HCFCs* 2020
* 10-year service tail for existing equipment
Response to Concerns

## Slide 16: Montreal Amendments September 1997
Moved Forward the Phase-out of Methyl Bromide from 2010 to 2005
Added Licensing Requirements for Use of New/Used/Recycled/Reclaimed ODS
Added Compliance Procedures for Calculating Consumption
Response to Concerns

## Slide 17: Beijing Amendments December 1999 (adjusted 2007)
Added Bromochloromethane and Established the Phase-out for 2002
Expanded Compliance Procedures for Calculating CFC/HCFC Compliance
Response to Concerns

## Slide 18: Kigali Amendments October 2016
U.S. Is a Signatory to the Amendment but Congress Did Not Ratify
Added HFC Greenhouse Gases (GHG) - HFCs Are Not ODS - Set Cap at 90% 2011-2013 Baseline - Set Graduated Reduction Schedule - Set Target (15% of Baseline) at 2036
Response to Concerns

## Slide 19: Clean Air Act Amendments (1990) Title VI - Stratospheric Ozone Protection
Class I ODS
  CFCs / Halons
  Carbon Tetrachloride
  Methyl Chloroform
  HBFCs
  Methyl Bromide
Class II ODS (HCFCs)
Production Phase-outs
  CFCs 31 Dec 95
  Halons 01 Jan 94
Response to Concerns

## Slide 20: National Defense Authorization Act for FY93 (PL102-484) Section 326
Congress Directed DoD to:
Review Contracts for Class I ODS
Determine if Can be Replaced
Allow Class I ODS in Contract only with the Approval of a Senior Acquisition Official
Response to Concerns

## Slide 21: DoDD 6050.9 13 February 1989
Identify Class I ODS Use and Criticality
Implement Conservation Measures
Conduct Research and Development
Eliminate ODS from MILSPECs/STDs
Buy & Store for Critical Applications Cancelled in 1998
Response to Concerns

## Slide 22: Response to Concerns
Army General Officer Steering Committees
07 July 89
30 April 90
19 December 91
Pursue Joint Research
Support Industry Programs
Fund Army R&D as a
Last Resort

## Slide 23: HQDA LTR 200-92-1 27 July 1992
Implemented DoD 6050.9
  Identified Army Responsibilities
    Established 21 Separate Policies
      Incorporated into AR 200-1
        EXPIRED
Response to Concerns

## Slide 24
FRAMEWORK FOR
PROGRAM EXECUTION
Assists in the Planning Process
Articulates Army ODS Policy
Provides Implementing Guidance
Identifies ODS Project Leadership
Integrates All Army ODS Efforts
Strategic Guidance and Planning
for
Eliminating Ozone-Depleting Chemicals
from
U.S. Army Applications
U.S. ARMY
ACQUISITION POLLUTION PREVENTION
SUPPORT OFFICE
Response to Concerns

## Slide 25
Army Regulation 200-1 21 March 1997
Eliminate Class I ODS by FY04
  Comply with PL 102-484, S326
    Document Requirements thru EPR
      Plan to Eliminate Class II ODS
UPDATED 13 December 2007
4-1.a.(3) Air Resources Policy
Eliminate dependency on ozone depleting substances.
Response to Concerns

## Slide 26
Early Policy Memos
AAE, Implementation of PL 102-484 S 326, 20 May 93
DASA(ESOH), Disposition of Excess ODCs at Army Installations, 18 Oct 94
ASA(IL&E), ODC Elimination at Army Installations, 13 Feb 96
Response to Concerns

## Slide 27
ACSIM Policy Memo
Elimination of the Dependency on
ODCs in Army Facilities, 3 Jul 1997
Commanders Responsible
Tenants Responsible to Comply
Class I ODS Out by the End of FY03
All Army Class I ODS Must Be Recovered
Alternatives Must Have EPA, ASG Clearance
No ODS in a Contract without SAO Approval
Response to Concerns

## Slide 28
ACSIM Policy Memo
14 January 1999
Installations Must Have ODS Plans by End of FY00
MACOMs Must Report Status EOY 1999 & 2000
Class I ODS Use Must Be Eliminated by 1 Nov 2003
Guide to Preparing
Ozone-Depleting Chemical
Elimination Plans
for Installations
Prepared for: Army
Acquisition Pollution Prevention Support Office
Response to Concerns

## Slide 29
AAE Policy Memo (I)
Eliminating the Dependency on ODCs
in Army Weapon Systems, 18 May 2000
Program Managers Responsible
No Class I ODS in New Systems
Alternatives Must Be AAE Approved
No ODS Solvent to Be Required or Used
All Class I ODS Must Be Recovered, Reused
Alternatives Must Have EPA, ASG Clearance
No Contract Can Require an ODS w/o Approval
Response to Concerns

## Slide 30
AAE Policy Memo (2)
Minimizing the Use of Ozone Depleting
Substances, 8 April 2013
No ODS in New Systems
No ODS from Reserve for FMS
No ODS Solvent Required or Used
No Buying Class II Refrigerants after 2014
Class I ODS Must Be Recovered – No Venting
SAO Approval Authority Delegated to PEOs
All Contracts Must Be Reviewed, Even COTS
PMs Using ODS Report Annually thru DASCs
Response to Concerns

## Slide 31
AAE Policy Memo (3)
Ozone Depleting Substances and Their
Alternatives, 17 May 2018
Units Authorized to Use ODS
No ODS from Reserve for FMS
No ODS in New Weapon Systems
No Commercial Procurement of Refrigerants
No Venting ODS or Hydrofluorocarbons (HFCs)
COTS, SBIR, software and services contracts without MILSPECs do not require ODS review
Cannot reinstall expired hydro-test fire bottles
Must remove portables w/expired service lives
Response to Concerns

## Slide 32
Army ODS Applications
FIRE SUPPRESSANTS
SOLVENTS
REFRIGERANTS

## Slide 33: Class I ODS Applications
HALONS
CFCs
Fire & Explosion Protection
General Surface Cleaning
Air Conditioning & Refrigeration

## Slide 34: Halon Applications
Ground Combat Vehicles
  Watercraft Engine Rooms
    Aviation Nacelles
        Facilities

## Slide 35
Ground
Combat Vehicles
Crew Compartment Explosion Protection
  Combat Survivability
Engine Compartment Fire Suppression
Abrams Handheld Fire Extinguishers

## Slide 36
M1 ABRAMS NBC FOX
M2/3 BRADLEY M9 ACE
M109 PALADIN
M551 SHERIDAN
M992 FAASV
Ground
Combat Vehicles

## Slide 37: Aviation
UH-1 EO-5 AH-6
RC-12 C-20 C-27
C-31 UC-35 C-37
CH-47 OH-58 UH-60
AH-64 TH-67 UH-72
CH-47
UH-60
AH-64
MI-24
Engine Nacelles
Hand-held
Fire
Extinguishers

## Slide 38: Watercraft
Landing Craft Utility (LCU) 1600
Landing Craft Utility (LCU) 2000
Landing Support Vehicle
Inland & Coastal Large Tug
Machinery Spaces
Flammable Storage
D O N E

## Slide 39: Facilities
Computer and Data Storage Rooms
Telecommunications Areas
Electronic Switch Gear Rooms
Uninterrupted Power Source (UPS)
Flight Simulators
D O N E

## Slide 40: Halon Categories
RESERVE SUPPORTED
Armor Turret/Crew Areas
Armor Engine Compartments
Aviation Engine Nacelles
Watercraft Engine Spaces
Handheld Fire Extinguishers *
NOT RESERVE SUPPORTED
        Facilities Fire Suppression

## Slide 41: CFC Applications
FACILITIES
FIELDED SYSTEMS
Air-Conditioning
Refrigeration
D O N E

## Slide 42: Air Conditioning
Facilities
Fielded Systems
Commercial
Industrial
Tactical Shelters
Tactical Vehicles
Watercraft
D O N E

## Slide 43: Refrigeration
Facilities
Fielded Systems
Cold Storage
Household
Kitchen Equipment
Food Service
Hospitals
Water Chillers
D O N E

## Slide 44: CFC Categories
RESERVE SUPPORTED
HMMWV Ambulance
NON-RESERVE SUPPORTED
        Field Refrigeration
        Facilities A/C & Refrigeration
D O N E

## Slide 45: Solvent Applications
Electronics Maintenance
General Metal Cleaning
Precision Metal Cleaning
Ordnance Manufacture
NBC Testing
D O N E

## Slide 46: Solvent Categories
RESERVE SUPPORTED
Nothing
NON-RESERVE SUPPORTED
        Everything
D O N E

## Slide 47: Class II ODS Applications
Halon Alternatives
HCFCs
Engine & Flightline Fire Suppression
Precision Cleaning
Air Conditioning & Cooling

## Slide 48
R-22 IN
FACILITIES AND
FIELDED SYSTEMS
Air-Conditioning
Cooling
Class II ODS Applications

## Slide 49: R-22 Air Conditioning
Facilities
Fielded Systems
COTS Building
Rooftop Systems
ECUs for Trailers,
Shelters and Tents

## Slide 50: R-22 Cooling
Facilities
Fielded Systems
Command Centers
Kitchen Equipment
Support, Training
and C3I Systems

## Slide 51: R-22 Categories
RESERVE SUPPORTED
ECUs (most of requirement)
Support, Training and C3I Systems
NON-RESERVE SUPPORTED
        Facilities Air Conditioning